## Slide 2
Project Overview
Abstract
Statement of the Problem
Objectives
Expected Outcome
Literature Review
Methodology
Results and Discussion
Recommendations and Conclusion
Outline

## Slide 3
Overview
It is estimated that 1.2 trillion kilograms of waste are produced across the world yearly.
A study done in Nairobi county revealed that garbage recycling has the ability to generate 13.5 billion Kenya shillings in Plastic bottles revenue.
In the JKUAT case study, the use of the different garbage bins for sorting trash has proven to be ineffective.
Waste sorting is an important process that precedes garbage recycling and disposal. The recyclable materials can even provide a steady revenue stream.
    Metal cans e.g. Aluminum cans.
    Glass bottles
Notes: 8/10/2018
2

## Slide 4
Abstract
Problem associated with garbage disposal
Current garbage management systems
Inefficiencies and gap associated with current systems
Solution adopted focusing on:
metal
glass
plastic
Garbage Control
Garbage Sorting
Promote Recycling
Notes: 8/10/2018
3

## Slide 5
[http://www.effectofglobalwarming.com/]
[http://www.iea.org/]
Problem Definition
Tons of garbage are produced around the school on a daily basis.
The Prevailing systems that are currently being used are ineffective.
Its from this data that the most profitable materials to recycle was decided upon.
Fig 1: Drainage System at the JKUAT Main gate

## Slide 6
Objectives
Main Objective:
To design and fabricate garbage waste separation and sorting system that will avail an avenue for the successful aggregation of recyclable waste for purposes of recycling and reuse.
Specific Objectives:
To design, fabricate and test a garbage separator that will provide a steady stream of waste that is fed one item at a time to the sorting system while removing unwanted particulate matter.
To design, fabricate and test a garbage sorter that will successfully identify and sort the waste as per the specified categories.
Notes: 8/10/2018
5

## Slide 7
Garbage waste sorting is an important process that precedes garbage recycling and disposal.
It is estimated that 1.2 trillion kilograms of waste are produced across the world yearly.
Garbage recycling has the ability to generate 13.5 billion Kenya shillings in revenue in Nairobi County.
At the end of this project, the following outcomes were expected:
Garbage separation- The mechanism will work such that from a heap of garbage loaded into the machine, itemization/singularization of the garbage will be achieved.
Garbage sorting-The sorting system will identify and categorize each garbage item according to the type of material.
The integration of the garbage separation and sorting system should be effective in sorting garbage.
Justification and Expected Outcome

## Slide 8
Literature Review
Material Recovery Facilities
The clean MRF and dirty MRF
How do they do it?
Trommel separators/drum screens
Eddy current separator
Induction sorting
Capacitive sensing sorting
Near infrared sensors (NIR)
X-ray technology
Fig 2: MRF

## Slide 9
Literature Review
Student Projects :
Fig 3:Automatic Waste Separator(AWS) Fig 4: The intelligent waste separator(IWS).
Gap Analysis:
Most of the these projects are designed to only sort the garbage if its only put into the garbage bin one item at a time.

## Slide 10
Methodology
The system is divided into two categories namely:
1. Garbage separation - this process entails the separation of accumulated trash into single entities to be fed into the system where sorting will take place.
2. Garbage sorting - this process involves the categorization of the provided single entity of waste. The categories of waste in sorting include plastics, metal can, glass and other waste.

## Slide 11
Design Considerations (General)
Size of the garbage
Weight of the garbage
Material
Cost
Geometry
Skill and expertise
Type of motion
Power requirements
Efficiency
Table 1:Bottle Sizes

## Slide 12
Design Considerations

## Slide 13
Design Calculations
Motor Sizing:
Fig 5: Rolling Wheel

## Slide 14
Garbage Separation
Fig 6 :2D Designs

## Slide 15
Garbage Separation (Integration)
Fig 7 :Garbage Separation

## Slide 16
Garbage Sorting Design
Fig 8 :Garbage Sorting

## Slide 17
Garbage Sorting (Integration)
Fig 9 :Garbage Sorting

## Slide 18
Redesigns
System Height
Metal Crushing Unit
Empty metal can collected at a Materials Recovery Facility are usually first separated into steel and aluminium, then crushed, baled and sent to re-
Processors.
Fig 8 :Metal Crushing Unit

## Slide 19
Design Considerations: Metal Crushing Unit
Method of actuation
22.2411 N to 88 N force required to crush all aluminum beverage from tests conducted.
A stroke length that is more than 170 mm and 115 mm which are the lengths of the largest and smallest metal cans that will be sorted.
2. Mounting
12V DC, stroke length- 200 mm, static load- 300N
which is sufficient to crush the metal cans being sorted, speed- 30mm/s.
Fig 9 :Linear Actuator

## Slide 20
Garbage Sorting and Separation (Integration)
Fig 10 :System Integration

## Slide 21
Fabrication Process
Table 3:Fabrication Process

## Slide 22
Mechanical Structure
Fig 11 :Mechanical Structure

## Slide 23
Electrical Circuit
Fig 12 :Etched PCB
Fig 13: Mounting of components

## Slide 24
Results and Discussion
Material Detection:
Material | Detection
Metal | 
Glass | 
Plastic | 

## Slide 25
Results and Discussion
Material | Detection Time | Detection Accuracy
Metal | 2 sec | 95%
Glass | 3 sec | 87%
Plastic | 5 sec | 77%
Values obtained from the number of materials used during testing.
How many bottles can be sorted in a minute?

## Slide 26
Challenges and Recommendations
Sensor range :limited range of between 2 mm- 5 mm.
2. Material separation and spacing-
Due to the difference in size of the garbage items being sorted, it was difficult to properly singularize and space the garbage items as
they got onto the conveyor.
3. Motor Torque and Conveyor Material
Lag of the conveyor when carrying heavier materials.
Challenges:
Recommendations:
1.The acquisition of sensors with the required range should be done earlier.
2. To effectively separate and space the garbage materials, there's need to add an extra mechanism that will facilitate the entry of materials in the conveyor one at a time.
3. The proper industrial grade conveyor belt should be used for the conveyor belt to avoid slip and sagging when in operation.

## Slide 27
Conclusions
Advantages of the system:
1. The separation and sorting of waste has introduced some autonomy hence reduced human effort.
2. The system can be modified to separate other kinds of waste which are not necessarily aluminum cans, plastic bottles, or glass.
The main objectives met include:
Garbage separation
Garbage sorting
Garbage sorting and separation

## Slide 28
Thank you for your attention.
Q/A

## Slide 29
Design of the V-shaped guideway

## Slide 30
Design of the slider

## Slide 31
Progress

## Slide 32
Progress

## Slide 33
Progress

## Slide 34
2)GARBAGE SORTING
Sorting System
The garbage from the separation system is delivered to the sorting system.
It consists of :
Delivery mechanism (Conveyor)
Detection unit
Blocking mechanism
Delivery mechanism
The design considerations include:
Type of motion
The dimensions/size of the garbage
The weight of the garbage

## Slide 35
Progress

## Slide 36
Design of the Rollers (driver)

## Slide 37
Progress

## Slide 38
Progress-bearing housing

## Slide 39
Design of the Rollers (driven)

## Slide 40
Progress

## Slide 41
Design of the blocking system

## Slide 42
Design of the Support Structure(conveyor)

## Slide 43
Progress

## Slide 44
Progress

## Slide 45
Motor Selection
Motors acquired include:
1 geared motor
3 Servo motors
Individual testing has been done.
The motor coupler has been acquired.

## Slide 46
Sensors acquired:
2 Capacitive sensors
1 inductive sensor
Phototransistor
Photoelectric Sensor
Individual testing and fine tuning to detect the materials being sorted is ongoing.
Detection Unit